Maryland State Highway Administration

Pilot Road Safety Audit Review Report:

MD 214

Project Description and Location: MD 214 (Central Avenue) from I-95/I-495 to Washington, D.C. Line is a 3.46 miles 6-lane urban arterial MD 214 runs parallel to the WMATA Metro Rail/Blue line and experiences a heavy volume of pedestrian traffic. This project is located in Prince George’s County, SHA District 3.

Audit Team Members: Two traffic engineers, one construction engineer, highway engineer and two community traffic safety coordinators. Resources for the RSAR included crash data, aerial photographs, traffic volumes, video logs, roadway friction data and transit/rider ship data. The audit was performed in January 2006.

Crash History: Number of vehicle crashes has declined from 217 to 166 between year 2002 and 2004, respectively. The number of reported pedestrian accidents, however, has remained unchanged at five incidents per year. The great majority of all accidents are intersection related, with a substantial number of crashes occurring at night and on wet surface. The AADT varies from 23,000 vpd to 59,000 vpd.

General Issues: Lack of ADA compliance for pedestrian amenities, heavy pedestrian volumes, speeding, outdating signing, too many access driveways, near side bus stops, interchange weaves, speeding, sporadic drainage deficiencies, mountable curbs where they shouldn’t be, restricted sight distances for left-turns and mid block pedestrian crossings.

Audit Findings: The audit was performed in a day time and on an average weekday. General findings are as follows:

| Problem | Potential Cause | Suggestions |
| --- | --- | --- |
| Pedestrian movements | Lack of ADA compliance | Install ADA amenities |
| In orderly maneuvers | Outdated signs and lack of it | Inventory and reevaluate |
| Vehicular crashes | Speeding | Reduce speed limit and install traffic calming measures |
| Mountable curbs as a safety hazard | Resurfacing with no milling | Install new curbs |
| Water/Ice accumulation | Insufficient drainage | Mill, level and resurface poor drainage areas |
| Damaged inlet grates | Not traffic bearing | Install traffic bearing grates |
| Restricted sign distances | Insufficient geometry for the prevailing speeds | Reduce speed limit |
| Weaving at MD 214 and I-95 | Substandard weave length | Reconfigure loop ramps |
| Restricted sight distance for left turns | Geometry | Reevaluate left-turn signal phasing at western entrance to Addison Plaza, Addison Road, Cindy Lane and Hill Road |
| Pedestrian confusion at crossings | Lack of understanding WK and FDW indications | Install pedestrian countdown signals |
| In orderly movements for yield control conditions | Lack of pavement markings and delineation | Install Shark Teeth across MD 332 at merge point EB MD 214; larger size Yield sign and better delineation of island |
| Pedestrian flow at bus stops | Nearside bus stops at Intersections | Reevaluate location of bus stops from near side to far side, throughout MD 214 |
| Unsafe maneuvers from access driveways | Too many access points | Consolidate access points |

Road Safety Audit Review Report: MD 494

Project Description and Location: MD 494 (Fairview Road) from MD 57 to Fairview Church Road is a two-lane rural roadway with no shoulders. The length of this section is two miles. This project is located in Washington County, SHA District 3.

Audit Team Members: The audit team consisted of two traffic engineers, one hydraulics engineer, one highway engineer, one community traffic safety coordinator and one human factors expert. Resources for the RSAR included crash data, traffic volumes, video logs, field observations, records of citizen complaints. The audit was performed in early January 2006, in day time hours only.

Crash History: A total of 16 crashes were reported on MD 494 from January 2002 to June 2005; ten crashes occurred at MD 57 and 6 crashes at Fairview Church Road. Eleven crashes occurred at night and on wet pavement. Ten of the total crashes were fixed-object type. Twelve of the total crashes occurred on a Friday, Saturday or Sunday. The majority of crashes are perceived to be caused by speeding and substandard curves.

General Issues: This section of MD 494 has two sharp curves with a 30 mph advisory speed.  It is perceived that both curves are not signed properly and the approach roadways lack adequate lighting and delineation. Furthermore, the roadway horizontal alignment appears to fail drivers’ expectancy as they approach the curves.

Audit Findings: During the audit period the pavement surface was dry. Speed limits in both directions are 55 mph, with 30 mph advisory speeds at curves General findings are as follows:

| Problem | Potential Cause | Suggestion |
| --- | --- | --- |
| Chevron signs are difficult to see on eastbound approach MD 494 to left hand curve | Alignment of roadway not too conducive to drivers’ expectancy | Relocate chevron signs |
| Alignment of Curve on eastbound approach of MD 494 | Right edge line and flare of traffic barrier could be misinterpreted by unfamiliar drivers | Re-stripe dashed edge line through intersection to delineate edge of road travel path. Install intersection lighting |
| Reverse curve signs on MD 494 at MD 57 | Signs not appropriate for the curve alignment | Replace reverse curve sign with turn or curve sign, based on results of Ball-Bank study |
| Fixed object crashes, striking traffic barrier on MD 494 | Possible lack of super-elevation and speeding | Perform super-elevation study and wedge and level to meet minimum requirements. Consider reducing speed limit |
| Warning signs on MD 494 | Outdated signs | Upgrade all warning signs per latest MUTCD guidelines—fluorescent yellow standard |
| Sight distance from MD 57 onto MD 494 | Alignment of intersection | Install stop line closer to intersection. Also consider a roundabout |
| Crashes at both Curves | Speeding | Consider reducing the speed limit. Also consider a roundabout |
| Conflict at intersection of MD 494 at Fairview Church Rd. | Limited sight distance for motorists making left onto Fairview Church Rd. | Reconfigure intersection to a T or a roundabout |
| Pavement markings between two curves | Lack of uniformity in pavement markings and delineation | Install wide edge lines throughout the limits of this section of MD 494 |
| Majority of crashes involved vehicles traveling eastbound, crossing the centerline and leaving the roadway | Speeding and failing to pay attention | Install centerline rumble strips |

Road Safety Audit Review Report: US 50

Project Description and Location: This section of US 50 begins at Phillip Morris Drive and ends at Walston Switch Road, in Wicomico County, SHA District 1. The length of this section is three miles, and consists of US 50 Business in its western limits from Phillip Morris Drive to the US 50/US 13 interchange and US 50 from west of Hobbs Road to Walston Switch road at its eastern limits.

Audit Team Members: The audit team consisted of one traffic engineer, one highway engineer, one maintenance engineer, one transportation planner, two community traffic safety coordinators and one human factors expert. Resources for the RSAR included crash data, existing roadway plans, traffic counts, video logs and field observations. The audit was performed in early January 2006, in day time hours only.

Crash History: A total of 74 crashes occurred in 2004, in this section. Rear-end and angle crashes accounted for 33 and 22-percent of the total crashes, respectively. The majority of crashes occurred on dry pavement and in day time hours. The speed limit on US 50 is 55 mph. SHA has recently installed rumble strips on the westbound approaches to Walston Switch Road and Hobbs Road, and flashing Signal Ahead signs on the westbound approach to Walston Switch Road and the eastbound approach to Hobbs Road.

General Issues: This section of US 50 experiences unusual delay at Tilghman Road; sporadic pedestrian movements in mid-blocks along US 50, across from shopping centers and hotels; lack of lighting along US 50; weaving from westbound US 50 to northbound Salisbury Bypass; a high accident intersection at Walston Switch Road; and high traffic volumes during the summer months.

Audit Findings: During the audit period the pavement surface was dry. General findings are as follows:

| Problem | Potential Cause | Suggestion |
| --- | --- | --- |
| Special event traffic conditions for the East Wicomico Little League | Increase in traffic volumes and unusual surges in traffic movements | Community outreach to the local communities and drivers |
| Substantial number of intersection crashes at US 50 and Walston Switch Road | Young drivers and failing to pay attention and yield right of way to other drivers | Outreach to students at the Wor/Wic Community College |
| Signals at Walston Switch Road and Hobbs Road are not necessarily expected by motorists | Great separation between signals on US 50; drivers may not expect to see signals | Install flashing “Signal Ahead” signs on eastbound Walston Switch Road and westbound Hobbs Road |
| Weaving from westbound US 50 to northbound Salisbury Bypass | Road geometry | Install advance signing under the US 50/MD 13 overhead sign on westbound US 50, indicating “RIGHT LANE” |
| Markings and sign control for weaving section from westbound US 50 to northbound Salisbury Bypass | Auxiliary lane markings may confuse drivers. Lack of Yield sign could may contribute to crashes | Change a portion of puppy tracks between Hobbs Road and the on-ramp to regular lane markings. Install a “Yield” sign on the on-ramp from eastbound US 50 Business |
| Restricted sight distance in eastbound crossover to Salisbury Bypass | Overgrown vegetation | Trim vegetation in median |
| Right turn from southbound Hobbs Road to US 50 | Uncontrolled movement | Signalize right turn movement and don’t allow with westbound US 50 |
| Confusion at the split of US 50 into the Salisbury Bypass | Roadway alignment | Geometric improvements to the existing split. Dualize the ramp to the Bypass. Redesign the interchange so that US 50 connects to US 50 rather than US 50 Business. |

Road Safety Audit Review Report: MD 31

Project Description and Location: This section of MD 31 is six miles long two-lane rural minor arterial. It begins at west of MD 140 and ends immediately west of MD 852S (Old New Windsor Pike), in Carroll County, SHA District 7. This section includes 12 intersections, two of which are signalized. The speed limit varies from 40 to 55 mph. Truck traffic accounts for approximately 20-percent of all traffic volumes.

Audit Team Members: The audit team consisted of one traffic engineer, one highway engineer, two transportation planners, and one community traffic safety coordinator. Resources for the RSAR included crash data, traffic counts, record of citizen complaints, an earlier traffic safety study, video logs and field observations. The audit was performed in early January 2006, in both daytime and nighttime hours.

Crash History: A total of 80 crashes have occurred between January 2000 and September 2003. Angle collisions are the most dominant type of accidents and occurred mostly at Windsor Drive, Long Drive, Long Valley Road and Old New Windsor Pike.  Rear-end crashes also accounted for 20 of the total crashes. Opposite direction crashes also occurred between the section of Medford and Byron Road.

General Issues: Primary complaints from citizens focus on traffic operations and safety; bus drivers waiting on the shoulders to start their routes in the morning , speeding throughout the arterial; and need for signals at intersections in residential developments on MD 31.  Also, there has been concern regarding increased residential developments in the areas of Tahoma Farm Road and Long Valley Road, as well as high truck volumes at Byron Road and the quarry at Medford Road and Stone Chapel Road.

Audit Findings: The audit team traveled the site during the AM and PM peak hours and observed traffic conditions throughout the day. General findings are as follows:

| Problem | Potential Cause | Suggestion |
| --- | --- | --- |
| Buses stopping on the shoulders with oversized truck loads having to go into the oncoming traffic lane to get around busses. | Bus drivers are arriving early to start bus pick-ups and wait on shoulder | Recommend contacting bus company to ask drivers to wait in more safe locations. |
| Opposite direction crashes in passing zones | Passing zones may not reflect the prevailing speeds | Examine the existing passing zones and make recommendation for upgrades |
| Yield sign at Byron Road | Not clear if proper sign is installed | Perform a warrant study for “Yield” versus a “Stop” sign control |
| Sight Distance at Wakefield Valley Road and south leg of Medford Road | Intersection Geometry | Consider relocating stop bar at Wakefield Valley Road and repaint stop bar on south leg of Medford Road, lengthen deceleration lanes |
| Frequent bicycle activities in the corridor | No allocated space in existing travel lanes | Install bicycle lanes with future safety improvements |
| Failed shoulder pavement | Truck traffic | Consider full depth patching in failed shoulder pavement |
| Guardrail end treatments and roadside slope protection | Substandard end treatments and changes in roadside conditions | Perform a guardrail safety study and upgrade sections and end treatments accordingly |
| Pedestrian facilities at Uniontown Road and Windsor Drive | ADA compatibility | Upgrade pedestrian facilities for ADA compliance |
| Unrestricted right-turn from Uniontown Road and Main Street | Sight distance onto westbound MD 31 | Evaluate restriction for right turns |
| Acceleration Lane at Medford Rd. | Short acceleration lane | Evaluate lengthening and widening accel. lane |
| TCDs on parallel section of Old New Windsor Road | Stop control into parallel road may not be the best type of control | Perform study for TCDs along the parallel roadway, specifically for stop control conditions |